- Preparation and Planning

  - Make a template

    - Draft the parameters

    - Draw the curves

    - Cut out template

  - Make the assembly workboard

    - Trace the template on plywood

    - Cut out workboard

    - Make the workboard shim and clamping shoe

- The Neck and Headpiece

  - Construct the neckblank

    - Lay out lines on the shaft

    - Make the scarf cut

    - True the scarf surfaces

    - Reduce the headstock thickness

    - Glue the scarf joint

    - Mark the shaft for the heelblock

    - Prepare the stacked heel pieces or heelblock

    - Glue the heelblock

    - Trim the neckshaft and height of the heelblock

    - Draft the outline of the fingerboard on the shaft

  - Fabricate the truss rod

    - Fold the rod

    - Thread the rod

    - Fabricate the cap

    - Wrap the rod

  - Cut out rod slot and neck joint

    - Lay out lines on the neckblank

    - Rout the slot

    - Cut the joint

  - Install the truss rod

    - Trim the veneer

    - Glue the veneer

  - Cut out the headpiece outline

    - Lay out the headpiece

    - Saw the outline

    - True the edges

    - Finish the crest

  - Drill the headpiece

  - Carve the heel

    - Lay out the heel cap and heel curve outline

    - Saw the heel profile

    - Ramp the heel

    - Concave the heel ramps

    - Carve the primary facets

    - Carve the secondary facets

    - Refine the carved heel

- The Plates

  - Joint the plates

    - Make a shooting board

    - Select the correct edges of the soundboard

    - Shoot the edge

    - Candle the edge

    - Joint the back plate

    - Joint the side plates

    - Dimension the side plates

  - Join the plates

    - Make a joining board

    - Position the plates and the blocks

    - Glue and press the soundboard halves

    - Join the back

  - Thickness the plates

    - Cut out the soundboard

    - Clean the faces

    - Plane the soundboard to thickness

    - Plane the back to thickness

    - Plane sides to thickness

- The Soundhole Rosette

  - Prepare rosette material

    - Select lines

    - Prepare pearl or marquetry purflings

  - Excavating the rosette channel

    - Lay out the rosette

    - Rout out or carve out the channel

  - Inlay the rosette

    - Pre-bend the lines

    - Glue in the lines

    - Glue in the pearl segments

    - Clean up

  - Cut out soundhole

- Soundboard bracing

  - Prepare the brace blanks

    - Split and dimension the brace blanks

    - Plane the blanks to dimension

    - Prepare the flat grafts

    - Arch the arched braces

  - Brace the soundboard

    - Make the bridge patch

    - Glue the bridge patch

    - Prepare, glue, shape upper transverse graft

    - Glue and shape flat braces

    - Glue and shape upper and lower face braces

    - Cut the X-brace lap joint

    - Glue and shape the X-brace

    - Glue the center seam diamonds

    - Glue the linen patch

    - Final graduation

- Side Bending

  - prepare and mark slats

  - bend the slats

- Soundbox assembly

  - Prepare and glue the headblock

    - Cut the joint into headblock

    - Align and pre-drill for the brads

    - Glue the soundboard to the neckshaft

  - Make and attach the tailblock

  - Trim the sides to length between the headblock & tailblock

  - Make the solid or kerfed linings

  - Apply linings to sides

  - Level the kerfed side edge

  - mark and notch the linings to accept the brace ends

  - glue the sides to the soundboard

  - trim and taper sides to final height

  - apply back linings to sides

  - prepare the lined edges to accept the back

  - Make the bridge block and upper face caul

  - Make the back

    - Slot center seam

    - Insert inlay

    - Make and install the back center seam graft

    - Make and arch the back braces

    - Slot center seam graft to accept back braces

    - Glue the back braces

    - Carve and refine back braces

  - Fit the back

    - Align and mark

    - Cut back the brace ends

    - Trim the back grafts

    - Trim the back overhang

  - Glue the back on

    - Apply glue to the edge and rope the back

    - Remove the soundbox from the workboard

  - Bind the guitar

    - Prepare and insert the end graft

    - Rout the binding and purfling ledges

    - Even the ledges

    - Prepare and pre-bend all binding and purfling materials

    - Fit and glue the bindings

    - Scrape the binding flush

- The Fingerboard

  - Make the fingerboard

    - True the billet

    - Mark the fret slots

    - Saw the fret slots

    - Taper the fingerboard to final outline

  - Glue the fingerboard to the neck

    - Mark the shaft

    - Glue and clamp the fingerboard

  - Fret the fingerboard

    - Arch the fingerboard

    - Install frets

    - File and bevel the fret ends

    - Level the frets

- Final Carving and Refining

  - Glue the heelcap

    - Prepare the heelcap

    - Glue the heelcap

  - Finish carve the neck

  - Inlay the emblem and bind the headpiece

  - Set the neck angle

    - Flatten the bearing surfaces on the sides

    - Fit neck into soundbox

    - Shave heel bearing surfaces to set angle

  - Refine all surfaces

    - Final scraping of plates

    - Fill end-gaps under frets

    - Install marker dots on fingerboard edge

    - Coarse sand the guitar

    - Round the bindings and all sharp edges

    - Final sanding

    - Mask fretboard and purflings on back and sides

- Finishing Neck and Soundbox with Lacquer

  - Fill the open pores

    - Pre-seal all surfaces to be filled

    - Prepare the filler

    - Apply the filler

    - Remove excess filler and clean up

  - Apply undercoats

    - Vacuum the guitar inside and out

    - Make and install shooting handle for soundbox

    - Apply one or two sealer coats

    - Scuff the sealer and vacuum

  - Apply the overcoats

    - Apply tinted lacquer undercoat if desired

    - Apply two or three lacquer top coats

    - Allow to dry thoroughly and level

    - Apply two to five lacquer top coats

    - Allow to dry three to seven days

  - Polish the finish

    - Dry sand with 320 No-Fill sandpaper

    - Wet sand with 500 Wet or Dry sandpaper

    - Polish with coarse compound

    - Polish with fine compound

- Attach the Neck

- The Bridge

  - Make the bridge

    - Square the billet and mark

    - Excavate the saddle slot

    - Drill for the bridge pin holes

    - Shape and refine the bridge

  - Glue the bridge

    - Locate the bridge on the soundboard

    - Scribe the bridge location

    - Tape around the bridge location

    - Scrape off finish with the tape

    - Insert the bridge block

    - Glue and clamp the bridge

    - Clean up glue squeeze-out

- Stringing and Setup

  - Dress and polish the frets and fingerboard

    - Final truing of frets

    - Recrown the frets

    - Dress the fret ends

    - Scrape the fingerboard

    - Sand the frets and fingerboard surface

    - Polish and oil fretboard

  - Setup the guitar

    - Drill through soundboard at bridge pin holes

    - Fit bridge pins

    - Cut bridge pin ramps

    - Fit the nut and saddle blanks into their slots

    - Preliminary shaping of nut and saddle

    - Install tuning machines

    - Install strings at bridge

    - Preliminary notches in the nut for strings

    - Bring the strings up to pitch and measure clearances

    - Final shaping of the nut

    - Final shaping of the saddle

    - Polish nut and saddle

    - Cut and apply pickguard

    - Prepare and apply maker’s label